## Slide 1: Voor aanzicht

## Slide 3: Summary of assignment
investigate the feasibility of using "wifi fingerprinting" to determine a person's location in indoor spaces.
evaluate multiple machine learning models to see which produces the best result.
make a recommendation to the client that would like ultimately develop an indoor locating app

## Slide 4: Data summary
Created 2013 by 20 different users with 25 Android Devices
3 Buildings, 4 or more floors
529 attributes with WiFi fingerprint (RSSI) values from -104 dBm -
            (extremely poor signal) to 0 dBm
Per building latitude, longitude, floor & relative position is given
19.937 records for training
1.111 records for validation
0
1
2
0
1
2
In average 8-25 WAP’s are detected on a single capture
and differs depending on environment & device

## Slide 5
WAP 001-519 (RSSI levels) | WAP520 (RSSI - intensity values | 521 (Neg. real- Longitude | 522 (Pos. real- Latitude | 523 (Integer value Altitude Floor 0-4) | 524 (cat. Integer) Building id | 525 space Id (cat. integer) | 526 Relative position for the space (cat. Integer) | 527 User id. Cat. Integer | 528 Phone ID. Android ID Cat. integer | 529 Time stamp Integer value
-104. – 0 (= poor – extremely good) | -104. – 0 (= poor – extremely good) | -7695.9387549299299000 | 4864745.7450159714 | Altitude in floors Inside the building | 0 - 2 | Office, Corridor, Classroom | 1 – inside space, 2 – outside space in front of the door of the space (corridor) | 0 USER0000 (Validation user – N/A) ID USER HEIGHT 1 USER0001 170 2 USER0002 176 3 USER0003 172 4 USER0004 174 5 USER0005 184 6 USER0006 180 7 USER0007 160 8 USER0008 176 9 USER0009 177 10 USER0010 186 11 USER0011 176 12 USER0012 158 13 USER0013 174 14 USER0014 173 15 USER0015 174 16 USER0016 171 17 USER0017 166 18 USER0018 162 | 0 Celkon A27 4.0.4(6577) 0 1 GT-I8160 2.3.6 8 2 GT-I8160 4.1.2 0 3 GT-I9100 4.0.4 5 4 GT-I9300 4.1.2 0 5 GT-I9505 4.2.2 0 6 GT-S5360 2.3.6 7 7 GT-S6500 2.3.6 14 8 Galaxy Nexus 4.2.2 10 9 Galaxy Nexus 4.3 0 10 HTC Desire HD 2.3.5 18 11 HTC One 4.1.2 15 12 HTC One 4.2.2 0 13 HTC Wildfire S 2.3.5 0,11 14 LT22i 4.0.4 0,1,9,16 15 LT22i 4.1.2 0 16 LT26i 4.0.4 3 17 M1005D 4.0.4 13 18 MT11i 2.3.4 4 19 Nexus 4 4.2.2 6 20 Nexus 4 4.3 0 21 Nexus S 4.1.2 0 22 Orange Monte Carlo 2.3.5 17 23 Transformer TF101 4.0.3 2 24 bq Curie 4.1.1 12 | 12:02:22 PM GMT +02
+100 (not detected) | +100 (not detected) | to | to | 0 - 4 |  |  |  |  |  | 
+100 = artificial value | +100 = artificial value | -7299.786516730871000 | 4865017.3646842018 |  |  |  |  |  |  | UNIX Time
Fingerprint
Building 0 | Building 1 | Building 2
Floor 1, space id 111, Rel. Pos. 2 | Floor 1 space id 111, Rel. Pos. 2 | Floor 2.1 space id 111, Rel. Pos. 2
Floor 2… | Floor 2… | Floor 2…
Floor 3… | Floor 3… | Floor 3…
Floor 4… | Floor 4… | Floor 4…
Predicting attributes for estimating position of user
21049 records = single record with 529 numeric elements
18 users, 20 (25 –Android) devices
19.937 training records
1.111 test records (525 & 526 & 527 empty with default value 0 in both fields and to simulate real localization system)
529 attributes, integer/real
933 reference points (places)
Regression
Space id like office, corridor, classroom
Infrastructure less approach by WAP’s
WLAN access points
-45dBm to 0dBm is insignificant and cover only 1.7% of total RSSI levels
-95dBm is also insignificant (2.3% of total RSSI measures)
Real world coordinates

## Slide 6: Summary (trainingData [ ,521:529])
LONGITUDE LATITUDE FLOOR BUILDINGID SPACEID RELATIVEPOSITION USERID
Min. :-7691 Min. :4864746 Min. :0.000 Min. :0.000 Length:19937 Min. :1.000 Min. : 1.000
1st Qu.:-7595 st Qu.:4864821 1st Qu.:1.000 1st Qu.:0.000 Class :character 1st Qu.:2.000 1st Qu.: 5.000
Median :-7423 Median :4864852 Median :2.000 Median :1.000 Mode :character Median :2.000 Median :11.000
Mean :-7464 Mean :4864871 Mean :1.675 Mean :1.213 Mean :1.833 Mean : 9.068
3rd Qu.:-7359 3rd Qu.:4864930 3rd Qu.:3.000 3rd Qu.:2.000 3rd Qu.:2.000 3rd Qu.:13.000
Max. :-7301 Max. :4865017 Max. :4.000 Max. :2.000 Max. :2.000 Max. :18.000
PHONEID
Min. : 1.00
1st Qu.: 8.00
Median :13.00
Mean :13.02
3rd Qu.:14.00
Max. :24.00
TIMESTAMP
Min: "2013-05-30 10:15:24"
1st Qu: "2013-06-12 16:50:18"
Median "2013-06-20 08:12:52"
Mean: "2013-06-16 22:20:50"
3rd Qu: "2013-06-20 09:37:26"
Max: "2013-06-20 14:15:45"

## Slide 7: test KNN-5 in EDA fase
Fit_long
k-Nearest Neighbors
1502 samples
529 predictor
Pre-processing: median imputation (525), remove (122)
Resampling: Cross-Validated (10 fold, repeated 1 times)
Summary of sample sizes: 1352, 1353, 1352, 1351, 1351, 1352, ...
Resampling results across tuning parameters:
k RMSE Rsquared MAE
5 13.25943 0.9885509 7.446795
7 15.20129 0.9849412 8.750156
9 16.84683 0.9814590 9.967150
RMSE was used to select the optimal model using the smallest value.
The final value used for the model was k = 5.

## Slide 8
1st iteration with KNN-5 model
Sample size 7500. Data partition 75/25
Per building (0, 1, 2)
For Latitude, Longitude, Floor
Pre-process
zv = identifies numeric predictor columns with a single value (i.e. having zero variance)
medianImpute = in case of missing values use median
TuneLength = 5, verboseIter = True,
preProcess = c(“zv”, “medianImpute”)

## Slide 9: 1st KNN-5 model results for Lat/Long
Fit_lat_B0 <- train(LATITUDE ~.,
data = training_B0_lat,
method = "kknn",
trControl=fitControl,
tuneLength = 5,
verboseIter = TRUE,
preProcess = c("zv", "medianImpute"))
Fit_lat_B0
saveRDS(Fit_lat_B0, file = "KNN_Fit_lat_B0.rds")
#k RMSE Rsquared MAE
#5 6.460450 0.9588620 3.660657
#Fit_lat_B0 postresample----
postResample(pred = predict(object = Fit_lat_B0,
newdata = testing_B0_lat),
obs = testing_B0_lat$LATITUDE)
# RMSE Rsquared MAE
# 6.7003103 0.9609583 4.0250448
Fit_lat_B1 <- train(LATITUDE~.,
data = training_B1_lat,
method = "kknn",
trControl=fitControl,
tuneLength = 5,
verboseIter = TRUE,
preProcess = c("zv", "medianImpute"))
Fit_lat_B1
saveRDS(Fit_lat_B1, file = "KNN_Fit_lat_B1.rds")
#k RMSE Rsquared MAE
#5 8.241445 0.9482391 4.979434
#Fit_lat_B1 postresample----
postResample(pred = predict(object = Fit_lat_B1,
newdata = testing_B1_lat),
obs = testing_B1_lat$LATITUDE)
# RMSE Rsquared MAE
# 6.7663285 0.9645302 4.4480253
Fit_lat_B2 <- train(LATITUDE~.,
data = training_B2_lat,
method = "kknn",
trControl=fitControl,
tuneLength = 5,
verboseIter = TRUE,
preProcess = c("zv", "medianImpute"))
Fit_lat_B2
saveRDS(Fit_lat_B2, file = "KNN_Fit_lat_B2.rds")
#k RMSE Rsquared MAE
#5 7.088801 0.9365169 3.989857
#Fit_lat_B2 postresample----
postResample(pred = predict(object = Fit_lat_B2,
newdata = testing_B2_lat),
obs = testing_B2_lat$LATITUDE)
# RMSE Rsquared MAE
# 6.0978035 0.9547484 3.4121850
Fit_long_B0 <- train(LONGITUDE~.,
data = training_B0_long,
method = "kknn",
trControl=fitControl,
tuneLength = 5,
verboseIter = TRUE,
preProcess = c("zv", "medianImpute"))
Fit_long_B0
saveRDS(Fit_long_B0, file = "KNN_Fit_long_B0.rds")
#k RMSE Rsquared MAE
#5 7.311088 0.9158382 4.482322
#Fit_long_B0 postresample----
postResample(pred = predict(object = Fit_long_B0,
newdata = testing_B0_long),
obs = testing_B0_long$LONGITUDE)
# RMSE Rsquared MAE
# 6.5256682 0.9337054 4.1474910
Fit_long_B1 <- train(LONGITUDE~.,
data = training_B1_long,
method = "kknn",
trControl=fitControl,
tuneLength = 5,
verboseIter = TRUE,
preProcess = c("zv", "medianImpute"))
Fit_long_B1
saveRDS(Fit_long_B1, file = "KNN_Fit_long_B1.rds")
#k RMSE Rsquared MAE
#5 8.538631 0.9698672 5.201769
#Fit_long_B1 postresample----
postResample(pred = predict(object = Fit_long_B1,
newdata = testing_B1_long),
obs = testing_B1_long$LONGITUDE)
# RMSE Rsquared MAE
# 7.890551 0.974103 5.055423
Fit_long_B2 <- train(LONGITUDE~.,
data = training_B2_long,
method = "kknn",
trControl=fitControl,
tuneLength = 5,
verboseIter = TRUE,
preProcess = c("zv", "medianImpute"))
Fit_long_B2
saveRDS(Fit_long_B2, file = "KNN_Fit_long_B2.rds")
#k RMSE Rsquared MAE
#5 9.455415 0.8973102 5.114687
#Fit_long_B2 postresample----
postResample(pred = predict(object = Fit_long_B2,
newdata = testing_B2_long),
obs = testing_B2_long$LONGITUDE)
# RMSE Rsquared MAE
# 9.2788440 0.9006733 4.9395021

## Slide 10: 1st KNN-5 model Lat/Long summary
Latitude
RMSE RSQ MAE
B0 6.700310 96.02481 4.025045
B1 6.700310 96.47526 4.448025
B2 6.097803 95.41785 3.412185
Longitude
RMSE RSQ MAE
B0 6.525668 93.29991 4.147491
B1 7.890551 97.40207 5.055423
B2 9.278844 90.12502 4.939502

## Slide 11: 1st KNN Floor B0 CF
In Building 0
79 predictions for floor 0 were True Positives
120 predictions for floor 1 were True Positives
116 predictions for floor 2 were True Positives
119 predictions for floor 3 were True Positives
In 12 cases floor 1 was misidentified as 0 & 1 times floor 2 was misidentified as 0
In 5 cases floor 0 was misidentified as being floor 1 & in 4 cases floor 2 was misidentified as 1
In 8 cases floor 1 was misidentified as being floor 2 & in 13 cases floor 3 was misidentified as 2
In 1 case floor 1 was misidentified as being floor 3 & in 15 cases floor 2 was misidentified as 3
Knn-5 can be optimized for floor Building 0 esp. floor 1, 2, 3
FLOOR

## Slide 12: 1st KNN Floor B1 CF
In Building 1
114 predictions for floor 0 were True Positives
38 predictions for floor 1 were True Positives
25 predictions for floor 2 were True Positives
12 predictions for floor 3 were True Positives
In 77 cases floor 1 was misidentified as 0, 95 were identied as floor 2 and 55 as floor 3 instead of 0
In 14 cases floor 0 was misidentified as being floor 1 & in 6 cases floor 2 was misidentified as 1
In 20 cases floor 1 was misidentified as being floor 2 & in 19 cases floor 3 was misidentified as 2
In 3 case floor 1 was misidentified as being floor 3 & in 9 cases floor 2 was misidentified as floor 3
B1 predictions for floor has an accuracy of 38.8% & esp. floor 1,2,3 is not predicted well
FLOOR

## Slide 13: 1st KNN Floor B2 Confusion Matrix
In Building 2
180 predictions for floor 0 were True Positives
179 predictions for floor 1 were True Positives
127 predictions for floor 2 were True Positives
251 predictions for floor 3 were True Positives
93 predictions for floor 4 were True Positives
In 10 cases floor 1 was misidentified as 0, 1 was identified as floor 2 and 3 as floor 3 instead of 0
In 3 cases floor 0 was misidentified as being floor 1 & in 8 cases floor 2 was misidentified as 1
In 1 case floor 1 was misidentified as being floor 2 & in 3 cases floor 3 as 2 & 2 cases floor 4 as 2
In 4 cases floor 1 was misidentified as being floor 3 & in 6 cases floor 4 was misidentified as floor 3
In 3 cases floor 3 was misidentified as being floor 4 .
Knn-5 was working quite good for predictions in Building 2
FLOOR

## Slide 14
2nd iteration with KNN-5 model
Data partition 75/25
Subset of all observations
Per building
For Latitude, Longitude, Floor
TuneLength = 5, verboseIter = True,
preProcess = c(“zv”, “medianImpute”)

## Slide 15: 2nd KNN-model summary training KPI’s
Fit_lat_B0
k-Nearest Neighbors
3939 samples
520 predictor
Pre-processing: median imputation (197), remove (323) Resampling: Cross-Validated (5 fold, repeated 1 times)
Summary of sample sizes: 3152, 3150, 3150, 3153, 3151
Resampling results across tuning parameters:
kmax RMSE Rsquared MAE
5 5.840343 0.9680237 2.806226
postResample(pred = predict(object = Fit_lat_B0,
+ newdata = testing_B0_lat),
+ obs = testing_B0_lat$LATITUDE)
RMSE Rsquared MAE
5.982871 0.967413 3.168045
> Fit_lat_B1
k-Nearest Neighbors
3898 samples
520 predictor
Pre-processing: median imputation (207), remove (313)
Resampling: Cross-Validated (5 fold, repeated 1 times)
Summary of sample sizes: 3118, 3119, 3118, 3119, 3118
Resampling results across tuning parameters:
kmax RMSE Rsquared MAE
5 6.506556 0.9679517 3.369182
postResample(pred = predict(object = Fit_lat_B1,
+ newdata = testing_B1_lat),
+ obs = testing_B1_lat$LATITUDE)
RMSE Rsquared MAE
5.8600480 0.9735459 2.9833834
Fit_lat_B2
k-Nearest Neighbors
7121 samples
520 predictor
Pre-processing: median imputation (201), remove (319)
Resampling: Cross-Validated (5 fold, repeated 1 times)
Summary of sample sizes: 5697, 5697, 5696, 5697, 5697
Resampling results across tuning parameters:
kmax RMSE Rsquared MAE
5 5.645028 0.9601617 2.843604
postResample(pred = predict(object = Fit_lat_B2,
newdata = testing_B2_lat),
obs = testing_B2_lat$LATITUDE)
RMSE Rsquared MAE
4.9402155 0.9682882 2.5529108
Fit_lONG_B0 k-Nearest Neighbors 3939 samples
520 predictor
Pre-processing: median imputation (198), remove (322)
Resampling: Cross-Validated (5 fold, repeated 1 times)
Summary of sample sizes: 3152, 3151, 3151, 3151, 3151
Resampling results across tuning parameters:
kmax RMSE Rsquared MAE
5 5.962481 0.9436714 3.075533
postResample(pred = predict(object = Fit_long_B0,
+ newdata = testing_B0_long),
+ obs = testing_B0_long$LONGITUDE)
RMSE Rsquared MAE
5.6387300 0.9480333 3.0377195
Fit_long_B1 k-Nearest Neighbors
3898 samples
520 predictor
Pre-processing: median imputation (204), remove (316)
Resampling: Cross-Validated (5 fold, repeated 1 times)
Summary of sample sizes: 3119, 3119, 3116, 3119, 3119
Resampling results across tuning parameters:
kmax RMSE Rsquared MAE
5 7.441228 0.9775019 3.678046
postResample(pred = predict(object = Fit_long_B1,
+ newdata = testing_B1_long),
+ obs = testing_B1_long$LONGITUDE)
RMSE Rsquared MAE
6.6183878 0.9819367 3.3280642
Fit_long_B2 k-Nearest Neighbors
7120 samples
520 predictor
Pre-processing: median imputation (202), remove (318)
Resampling: Cross-Validated (5 fold, repeated 1 times)
Summary of sample sizes: 5695, 5697, 5696, 5697, 5695
Resampling results across tuning parameters:
kmax RMSE Rsquared MAE
5 7.577559 0.9354733 3.559215
postResample(pred = predict(object = Fit_long_B2,
+ newdata = testing_B2_long),
+ obs = testing_B2_long$LONGITUDE)
RMSE Rsquared MAE
7.3556032 0.9404916 3.3675497

## Slide 16: 2nd KNN B0
FLOOR
KNNB0Floor Model
k-Nearest Neighbors
3939 samples
520 predictor
4 classes: '0', '1', '2', '3'
Pre-processing: median imputation (196), remove (324)
Resampling: Cross-Validated (5 fold, repeated 1 times)
Summary of sample sizes: 3151, 3151, 3151, 3152, 3151
Resampling results across tuning parameters:
kmax Accuracy Kappa
5 0.9185105 0.8910259
7 0.9207948 0.8941163
9 0.9218100 0.8954735
11 0.9223176 0.8961545
13 0.9223176 0.8961545
kappa_KNNB0Floor Confusion Matrix
value ASE z Pr(>|z|)
Unweighted 0.8833 0.010453 84.5 0
Weighted 0.9242 0.007019 131.7 0
Accuracy 32.25558
In Building 0
232 predictions for floor 0 were True Positives
323predictions for floor 1 were True Positives
316 predictions for floor 2 were True Positives
325 predictions for floor 3 were True Positives
In 26 cases floor 1 was misidentified as 0 & 1 times floor 2 was misidentified as 0
In 10 cases floor 0 was misidentified as being floor 1 & in 15 cases floor 2 was misidentified as 1
In 10 cases floor 1 was misidentified as being floor 2 & in 20 cases floor 3 was misidentified as 2
In 2 case floor 1 was misidentified as being floor 3 & in 28 cases floor 2 was misidentified as 3
Floor prediction in Building 0 has a low accuracy

## Slide 17: 2nd KNN B1
In Building 1
302 predictions for floor 0 were True Positives
69 predictions for floor 1 were True Positives
25 predictions for floor 2 were True Positives
23 predictions for floor 3 were True Positives
In 278 cases floor 1 was misidentified as 0 & 257 times floor 2 + 140 times floor 3 was misidentified as 0
In 35 cases floor 0 was misidentified as being floor 1 & in 11 cases floor 2 was misidentified as 1
In 72 cases floor 3 was misidentified as floor 2 while being 3
In 29 cases floor 1 was misidentified as being floor 3 & in 23 cases floor 2 was misidentified as 3
FLOOR
KNNB1Floor Model
k-Nearest Neighbors
3939 samples
520 predictor
4 classes: '0', '1', '2', '3'
Pre-processing: median imputation (196), remove (324)
Resampling: Cross-Validated (5 fold, repeated 1 times)
Summary of sample sizes: 3150, 3151, 3152, 3151, 3152
Resampling results across tuning parameters:
kmax Accuracy Kappa
5 0.9111391 0.8811726
7 0.9157089 0.8873319
9 0.9154551 0.8869937
11 0.9154551 0.8869956
13 0.9154551 0.8869956
kappa_KNNB1Floor Confusion Matrix
    value ASE z Pr(>|z|)
Unweighted 0.08894 0.01225 7.258 3.915e-13
Weighted 0.15751 0.01364 11.548 7.518e-31
Accuracy
Often floors are identified as 0, while being 1, 2 or 3

## Slide 18: 2nd KNN B2
FLOOR
KNNB2Floor Model
k-Nearest Neighbors
7120 samples
520 predictor
5 classes: '0', '1', '2', '3', '4'
Pre-processing: median imputation (201), remove (319)
Resampling: Cross-Validated (5 fold, repeated 1 times)
Summary of sample sizes: 5695, 5697, 5697, 5696, 5695
Resampling results across tuning parameters:
kmax Accuracy Kappa
5 0.9588484 0.9474698
7 0.9603923 0.9494419
9 0.9601116 0.9490859
11 0.9601116 0.9490859
13 0.9601116 0.9490859
kappa_KNNB2Floor Confusion Matrix
value ASE z Pr(>|z|)
Unweighted 0.9607 0.004529 212.1 0
Weighted 0.9759 0.002948 331.0 0
Accuracy 96.92243
In Building 2
478 predictions for floor 0 were True Positives
526 predictions for floor 1 were True Positives
356 predictions for floor 2 were True Positives
665 predictions for floor 3 were True Positives
274 predictions for floor 4 were True Positives
In 17 cases floor 1 was misidentified as 0 & 3 times floor 2 was misidentified as 0
In 5 cases floor 0 was misidentified as being floor 1 & in 18 cases floor 2 was misidentified as 1
In 4 cases floor 1 was misidentified as being floor 2 & in 9 cases floor 3 was misidentified as 2
In 5 case floor 1 was misidentified as being floor 3 & in 15 cases floor 2 was misidentified as 3
In 2 case floor 2 was misidentified as being floor 4 & in 1 case floor 3 was misidentified as 4
Knn-5 was working quite good for predictions in Building 2

## Slide 19: 2nd KNN-5 model Lat/Long/Floor KPI summary
2nd run Latitude
RMSE RSQ MAE
B0 5.982871 96.71153 3.168045
B1 5.982871 97.21531 2.983383
B2 4.940216 96.81935 2.552911
2nd run Longitude
RMSE RSQ MAE
B0 5.638730 94.79819 3.037719
B1 6.618388 98.19182 3.328064
B2 7.355603 94.04222 3.367550
FLOOR accuracy
B0 91.29771
B1 32.25558
B2 96.92243
FLOOR kappa
B0 Weighted 0.883266749
B0 ASE 0.010453337
B1 Weighted 0.088937612
B1 ASE 0.012252931
B2 Weighted 0.960692577
B2 ASE 0.004528678
1st run Latitude
RMSE RSQ MAE
B0 6.700310 96.02481 4.025045
B1 6.700310 96.47526 4.448025
B2 6.097803 95.41785 3.412185
1 st run Longitude
RMSE RSQ MAE
B0 6.525668 93.29991 4.147491
B1 7.890551 97.40207 5.055423
B2 9.278844 90.12502 4.939502

## Slide 20: Pre-liminary conclusions 2nd KNN model
Focus is to improve the predictions for Building 1.
And have a higher accuracy without downsizing the KPI’s for other Buildings.
Data represents data for Building 0, 1 & 2. Building 1 is therefore in the middle and between 0 & 2
In building 1 its difficult to predict the correct floor and its often therefore predicted as a lower floor.
Therefore:
Check distribution of signals
Check signals per user for the building
Check signal per phone for the buildings
Plot signals for the buildings to see coverage and if taken in or outside the room
3d plot signals per floor in the building
Plot signal strength for good, medium and bad for the buildings

## Slide 21
Data manipulation executed
Detected columns with only 100 values and removed them (using function x, select = unique length)
Detected rows with 100 values and removed them
Set Floor, building ID, Relative position, user id & phone id to factor. Left Timestamp as is (before converted)
Changed WAP signals to absolute values
  by adding +105 and after converting 100 to -105 and so that no signal is 0 and the highest is 104

## Slide 22: Distribution of WAP signals

## Slide 23: Another check longitude / latitude
Where did user log in (red is outside room, black is inside room)

## Slide 24: Check coverage per building per floor
Building 1 Log in Points
Building 2 Log in Points

## Slide 25: Signal check per building
Good Signal
Medium Signal
Bad Signal

## Slide 26: Users linked to Building 0

## Slide 27: Users linked to Building 1

## Slide 28: Users linked to Building 2

## Slide 29: How many locations have a user registered

## Slide 30: Number of locations registered by Phone id

## Slide 31
3rd iteration with KNN-5 model + RF
Data partition 75/25
Subset of all observations
Per building
For Latitude, Longitude, Floor
TuneLength = 5, verboseIter = True,
preProcess = c(“zv”, “medianImpute”)

## Slide 32: 3rd KNN-model Lat/Long/Floor KPI summary
Latitude
RMSE RSQ MAE
B0 4.200349 98.38193 2.067570
B1 4.200349 98.62613 1.977748
B2 3.650701 98.32693 1.846340
Longitude
RMSE RSQ MAE
B0 3.245267 98.27749 1.613786
B1 3.746984 99.42940 1.248799
B2 4.269281 97.96087 1.841995
FLOOR accuracy
B0 98.09160
B1 36.22964
B2 98.94157
kappa B0
FLOOR kappa
1 0.9969313489
2 0.0017695433
3 -0.0029030734
4 0.0016738360
5 0.9994596997
6 0.0005401941
kappa B1
kappa B2

## Slide 33: 3rd KNN B0
FLOOR
KNNB0Floor Model
k-Nearest Neighbors
3939 samples
520 predictor
4 classes: '0', '1', '2', '3'
Pre-processing: median imputation (196), remove (324)
Resampling: Cross-Validated (5 fold, repeated 1 times)
Summary of sample sizes: 3151, 3151, 3151, 3152, 3151
Resampling results across tuning parameters:
kmax Accuracy Kappa
5 0.9185105 0.8910259
7 0.9207948 0.8941163
9 0.9218100 0.8954735
11 0.9223176 0.8961545
13 0.9223176 0.8961545
kappa_KNNB0Floor Confusion Matrix
value ASE z Pr(>|z|)
Unweighted 0.8833 0.010453 84.5 0
Weighted 0.9242 0.007019 131.7 0
In Building 0
259 predictions for floor 0 were True Positives
337 predictions for floor 1 were True Positives
348 predictions for floor 2 were True Positives
325 predictions for floor 3 were True Positives
In 9 cases floor 2 was misidentified as 3

## Slide 34: 3rd KNN B1
In Building 1
338 predictions for floor 0 were True Positives
369predictions for floor 1 were True Positives
346 predictions for floor 2 were True Positives
223 predictions for floor 3 were True Positives
FLOOR
kappa_KNNB1Floor Confusion Matrix
    value ASE z Pr(>|z|)
Unweighted 0.08894 0.01225 7.258 3.915e-13
Weighted 0.15751 0.01364 11.548 7.518e-31

## Slide 35: 3rd KNN B2
FLOOR
KNNB2Floor Model
k-Nearest Neighbors
7120 samples
520 predictor
5 classes: '0', '1', '2', '3', '4'
Pre-processing: median imputation (201), remove (319)
Resampling: Cross-Validated (5 fold, repeated 1 times)
Summary of sample sizes: 5695, 5697, 5697, 5696, 5695
Resampling results across tuning parameters:
kmax Accuracy Kappa
5 0.9588484 0.9474698
7 0.9603923 0.9494419
9 0.9601116 0.9490859
11 0.9601116 0.9490859
13 0.9601116 0.9490859
kappa_KNNB2Floor Confusion Matrix
value ASE z Pr(>|z|)
Unweighted 0.9607 0.004529 212.1 0
Weighted 0.9759 0.002948 331.0 0
In Building 2
477predictions for floor 0 were True Positives
533 predictions for floor 1 were True Positives
385predictions for floor 2 were True Positives
667 predictions for floor 3 were True Positives
275 predictions for floor 4 were True Positives
In 17 cases floor 1 was misidentified as 0 & 3 times floor 2 was misidentified as 0
In 5 cases floor 0 was misidentified as being floor 1 & in 18 cases floor 2 was misidentified as 1
In 4 cases floor 1 was misidentified as being floor 2 & in 9 cases floor 3 was misidentified as 2
In 5 case floor 1 was misidentified as being floor 3 & in 15 cases floor 2 was misidentified as 3
In 2 case floor 2 was misidentified as being floor 4 & in 1 case floor 3 was misidentified as 4

## Slide 36: 1st Random Forest model Lat/Long/Floor KPI summary
Latitude
RMSE RSQ MAE
B0 4.200349 98.38193 2.067570
B1 4.200349 98.62613 1.977748
B2 3.650701 98.32693 1.846340
Longitude
RMSE RSQ MAE
B0 3.245267 98.82977 1.739514
B1 4.346220 99.23230 2.420201
B2 4.437505 97.79701 2.424726
FLOOR accuracy
B0 99.77099
B1 28.70442
B2 9894.15749
Kappa Accuracy ASE
B0
Unweighted 0.9969 0.001770 563.4
Weighted 0.9981 0.001098 909.4
B1
Unweighted -0.002903 0.001674
Weighted -0.003264 0.001880
B2
Unweighted 0.9995 0.0005402
Weighted 0.9997 0.0002822
FLOOR kappa
1 0.9969313489
2 0.0017695433
3 -0.0029030734
4 0.0016738360
5 0.9994596997
6 0.0005401941

## Slide 37: 1st RF B0
FLOOR
RFB0Floor Model
Confusion Matrix and Statistics
predictions_RFB0Floor 0 1 2 3
0 258 0 0 0
1 2 343 1 0
2 0 0 359 0
3 0 0 0 347
Overall Statistics
Accuracy : 0.9977
95% CI : (0.9933, 0.9995)
No Information Rate : 0.2748
P-Value [Acc > NIR] : < 2.2e-16
Kappa : 0.9969
kappa_RFB0Floor Confusion Matrix
value ASE z Pr(>|z|)
Unweighted 0.9969 0.001770 563.4 0
Weighted 0.9981 0.001098 909.4 0
In Building 0
258 predictions for floor 0 were True Positives
343predictions for floor 1 were True Positives
359 predictions for floor 2 were True Positives
347 predictions for floor 3 were True Positives
In 26 cases floor 1 was misidentified as 0 & 1 times floor 2 was misidentified as 0
In 2 cases floor 0 was misidentified as being floor 1 & in 1 case floor 2 was misidentified as 1

## Slide 38: 1st RFB1
In Building 1
0 predictions for floor 0 were True Positives
370 predictions for floor 1 were True Positives
0 predictions for floor 2 were True Positives
0 predictions for floor 3 were True Positives
In 340 cases floor 1 was misidentified as 0 & 349 times floor 2 + 227 times floor 3 was misidentified as 0
Other floors could hardly be predicted
Often floors are identified as 0, while being 1, 2 or 3
FLOOR
KNNB1Floor Model
Confusion Matrix and Statistics
predictions_RFB1Floor 0 1 2 3
0 0 0 0 0
1 340 370 349 227
2 0 0 0 0
3 0 3 0 0
Overall Statistics
Accuracy : 0.287
95% CI : (0.2625, 0.3126)
No Information Rate : 0.2894
P-Value [Acc > NIR] : 0.5835
Kappa : -0.0029
kappa_RFNB1Floor Confusion Matrix
    value ASE z Pr(>|z|)
    Unweighted -0.002903 0.001674 -1.734 0.08285
    Weighted -0.003264 0.001880 -1.736 0.0825031

## Slide 39: 1st RF B2
FLOOR
RFB2Floor Model
Confusion Matrix and Statistics
predictions_RFB2Floor 0 1 2 3 4
0 478 0 0 0 0
1 0 538 0 0 0
2 0 0 393 0 0
3 0 0 1 677 0
4 0 0 0 0 275
Overall Statistics
Accuracy : 0.9996
95% CI : (0.9976, 1)
No Information Rate : 0.2866
P-Value [Acc > NIR] : < 2.2e-16
Kappa : 0.9995
kappa_RFB2Floor Confusion Matrix
value ASE z Pr(>|z|)
Unweighted 0.9995 ` 0.0005402 1850 0
Weighted 0.9997 0.0002822 3542 0
In Building 2
478 predictions for floor 0 were True Positives
538 predictions for floor 1 were True Positives
393 predictions for floor 2 were True Positives
677 predictions for floor 3 were True Positives
275 predictions for floor 4 were True Positives

## Slide 40: 3rd KNN-5 model compared to RF 1st model
Latitude
RMSE RSQ MAE
B0 4.200349 98.38193 2.067570
B1 4.200349 98.62613 1.977748
B2 3.650701 98.32693 1.846340
Longitude
RMSE RSQ MAE
B0 3.245267 98.27749 1.613786
B1 3.746984 99.42940 1.248799
B2 4.269281 97.96087 1.841995
KPI’s KNN
KPI’s Random Forest
Latitude
RMSE RSQ MAE
B0 2.277268 99.52439 1.314716
B1 2.277268 99.59617 2.151043
B2 3.325760 98.61151 1.990321
Longitude
RMSE RSQ MAE
B0 3.245267 98.82977 1.739514
B1 4.346220 99.23230 2.420201
B2 4.437505 97.79701 2.424726
FLOOR RF
Accuracy
B0 99.77099
B1 28.70442
B2 98.15749
FLOOR KNN
Accuracy
B0 98.09160
B1 36.22964
B2 98.94157
Kappa ->
Kappa ->

## Slide 41
FLOOR RF
Accuracy
B0 99.77099
B1 28.70442
B2 98.15749
FLOOR KNN-11
Accuracy
B0 98.09160
B1 98.99147
B2 98.94157
KNN-5 compared to RF 1st model compared to KNN-11
Kappa ->
FLOOR KNN-5
Accuracy
B0 91.29771
B1 32.25558
B2 96.92243
FLOOR KNN-11 Kappa
B0
B1
B2
value ASE z Pr(>|z|)
Unweighted 0.9744 0.005067 192.3 0
Weighted 0.9836 0.003328 295.5 0
value ASE z Pr(>|z|)
Unweighted 0.9864 0.003749 263.1 0
Weighted 0.9914 0.002376 417.2 0
value ASE z Pr(>|z|)
Unweighted 0.9865 0.002688 367.1 0
Weighted 0.9910 0.001951 507.9 0
FLOOR kappa
B0 Weighted 0.883266749
B0 ASE 0.010453337
B1 Weighted 0.088937612
B1 ASE 0.012252931
B2 Weighted 0.960692577
B2 ASE 0.004528678

## Slide 42: Train KNN-5 compared to RF 1st model compared to KNN-11
Latitude
RMSE RSQ MAE
B0 4.200349 98.38193 2.067570
B1 4.200349 98.62613 1.977748
B2 3.650701 98.32693 1.846340
Longitude
RMSE RSQ MAE
B0 3.245267 98.27749 1.613786
B1 3.746984 99.42940 1.248799
B2 4.269281 97.96087 1.841995
KNN-5
Random Forest
Latitude
RMSE RSQ MAE
B0 2.277268 99.52439 1.314716
B1 2.277268 99.59617 2.151043
B2 3.325760 98.61151 1.990321
Longitude
RMSE RSQ MAE
B0 3.245267 98.82977 1.739514
B1 4.346220 99.23230 2.420201
B2 4.437505 97.79701 2.424726
KNN-11
Latitude
RMSE RSQ MAE
B0 4.2003490 0.9840869 2.06757
B1 4.8582787 0.9819695 2.0469997
B2 3.6507010 0.9833021 1.8463397
Longitude
RMSE RSQ MAE
B0 3.2758884 0.9825139 1.56748
B1 4.7377253 0.9909077 1.83818
B2 4.9858825 0.9731629 1.79484

## Slide 43
Predict with KNN-11 on validation data
Subset of all observations
Per building
For Latitude, Longitude, Floor
10fold CV, number = 10, repeat = 2
TuneLength = 10, verboseIter = True,
preProcess = c(“zv”)

## Slide 44: Latitude / Longitude KPI’s prediction KNN-11
Latitude RMSE RSQ MAE
B0 12.01272 85.79767 6.694701
B1 13.02912 86.19981 7.625970
B2 13.81677 76.50689 8.547353
Longitude RMSE RSQ MAE
B0 9.356922 87.15947 5.698902
B1 11.776899 93.36969 7.411041
B2 13.740808 80.83327 8.785949

## Slide 45: KPI’s Floor prediction based on KNN-11

## Slide 46: Check predicted (1st) long/lat

## Slide 47: KPI’s Floor prediction based on KNN-11

## Slide 48: Check predicted (2nd) long/lat

## Slide 49: 2nd Predicted check coverage per floor B0
Training Validation

## Slide 50: 2nd Predicted check coverage per floor B1
Building 1 Log in Points
Training Validation

## Slide 51: 2nd Predicted check coverage per floor B2
Building 2 Log in Points
Training Validation

## Slide 52
Predict with KNN-5, Kernel = triangular
Subset of all observations
Per building
For Latitude, Longitude, Floor
fitControl <- trainControl(method = "repeatedcv", number = 5, repeats = 1)
tuneGrid <- expand.grid(kmax =
1:11, # allows to test a range of k values
distance = 1:10, # allows to test a range of distance values
kernel = 'triangular')
TuneLength = 5, verboseIter = True,
preProcess = c(“zv”)

## Slide 53: KPI’S TRAINING MODEL KNN-5 KERNEL ‘TRIANGULAR’
Latitude K/D RMSE RSQ MAE
B1 1 4.594654 0.9841134 1.345218
Longitude K/D RMSE RSQ MAE
B1 1 5.042662 0.9897146 1.479346
Floor K/D Accuracy Kappa
B1 0.9989664 0.9986084

## Slide 54: KPI’S prediction KNN-5 KERNEL ‘TRIANGULAR’ B1
Latitude RMSE RSQ MAE
B1 13.90938 84.27212 8.087321
Longitude RMSE RSQ MAE
B1 12.95162 91.981 7.870612
Floor prediction is improved for accurate floors, however errors in predicting floor 3 & 2 stayed the same
Lat/long prediction did not improve on any KPI

## Slide 55: CONCLUSIONS & RECOMMENDATIONS
It is possible to locate a person in a building and roughly on a floor.
However if directions on room level are required the positioning need improvement to become more accurate.
Both Knn as RF perform quite good but differ per building floor
Improve the WiFi signal strength and make sure it is not interfering with other signals. Also make sure the signal is unique and consistent to Improve learning algorithms.
Consider to use best performing model per building and/or floor
investigate the feasibility of using "wifi fingerprinting" to determine a person's location in indoor spaces.
evaluate multiple machine learning models to see which produces the best result.
make a recommendation to the client that would like ultimately develop an indoor locationing app